## Slide 1
17/06/2025
Conall DE PAOR
1st year PhD student
ISAE-SUPAERO, DCAS, SaCLaB
ALTEN SO
ANRT
Supervisors : Stéphanie LIZY-DESTREZ, Joan-Pau SANCHEZ-CUARTIELLES, Julien LAFFORGUE, Sebastien MAES
MONEYBALL
NEW SIZING RULES AND ALGORITHMS FOR UNMANNED LUNAR LANDERS

## Slide 2: Contents
17/06/2025
Context – Why Size Unmanned Lunar Landers
Methods – Statistical Models and Sizing Algorithms
Results – Sizing Case Studies
Conclusion

## Slide 3: Context – The High Cost of Space Systems
17/06/2025
A key variable: The Life Cycle Cost:
Harrison Schmitt in 1972
257 Billion USD (2020) [1] Samples 671 Million USD/kg Earth Diamonds: 20.8M$/kg[2]
International Space Station
150 Billion USD (2010) [3]
Galileo Constellation
Block 1 : €953M (2010)[4]
Equivalent mass of gold: €462M [5]
To enable more like this, it needs to be cheaper

## Slide 4: Context – The High Cost of Space Systems
17/06/2025
A key to control costs: Estimate
Eilingsfeld F. Cost Engineering Lectures 2019 [3]

## Slide 5: Context – How to Estimate Cost and Why Size
17/06/2025
Order of Magnitude Estimation
Component list
Parametric Cost Estimation Models (CEMs)
QuickCost
NAFCOM
Advanced Mission Cost Model
Small Spacecraft Cost Model
TruePlanning
All these CEMs require the mass properties of the (sub)system as an input
Even better at subsystem level

## Slide 6: Context – Why Study Unmanned Lunar Landers
17/06/2025
Chart: Proportion of Manned vs. Unmanned Landers 1966 - 2025
| manned | unmanned
 | 7 | 36

## Slide 7: Current Topic – Mass Estimation of Lunar Landers
17/06/2025
Lunar Lander
Sizing Algorithm
Cost estimation
Study Objective:
Study case: lunar missions

## Slide 8: Methods – Statistical Models and Sizing Algorithms
17/06/2025
Application case: Lunar Surface Missions
How to approach this mass estimation problem: Reference Models
The Generic Lander Model
Single stage
Unmanned
+ +
LOX-LH2, LOX-LCH4, N2O4-AZ
The Generic Mission Model
Begin at LLO
Land on the surface with all payload
Return to LLO with some payload
Sets the delta-V
LLO
Surface
Phase
1
approach
0
Orbit
2
Descent & Landing
3
Payload deployment
4
Liftoff &
Orbit insertion
5
Orbit
Avionics
Propulsion
Structure
Power
Thermal
Other

## Slide 9: Methods – Statistical Models and Sizing Algorithms
17/06/2025
+ +
Solution: find additional relations using statistics
First: for system level mass properties
Unknown
known

## Slide 10: Methods – Databases
17/06/2025
System masses DB (#35)
(Almost) all flight models
Subsystem masses DB (#12)
Flown landers and concepts
(payload for manned landers is ascent stage)

## Slide 11: Results – Sizing Rules
17/06/2025
For the system masses:
Dry mass + payload mass [kg]

## Slide 12: Results – Sizing Rules
17/06/2025
For the subsystem masses: multiple linear regression, and bottom up sizing
Component level
Problems with outliers: Single linear regression used also

## Slide 13: Sizing Algorithm
17/06/2025
11 – Algorithms tested
Measured by median absolute error

## Slide 14: Results – Validation
17/06/2025
Resizing of the J-series Apollo LM. Algo No. 7 N2O4/AZ
=
all LM values from Apollo by the Numbers (Orloff 1996)
Good estimation of system level masses
Some large errors in ss sizing

## Slide 15: Results – Validation
17/06/2025
Resizing all landers in the DB. The best performers: all single linear regressors

## Slide 16: Conclusion
17/06/2025
Contributions:
  Most up to date published lunar lander database used for sizing rule derivation.
  Algorithms to size lunar landers to the subsystem level using only and
Future Work
  Must improve subsystem mass estimates
  Uncertainty propagation through the sizing algorithm and progressive estimation starting with the highest could improve subsystem mass estimates.

## Slide 17: References
17/06/2025
Amos, J., 2010. EU awards Galileo satellite‑navigation contracts. BBC News, 7 January. Available at: http://news.bbc.co.uk/2/hi/science/nature/8442090.stm]
StoneAlgo (2024) Diamond Prices – Real-Time Market Trends. Available at: https://www.stonealgo.com/diamond-prices/?srsltid=AfmBOooDezL1x8X3j9bA7wr0FFT2uVo1hgZrP4pOa6aAj3RQ3cCIizXn (Accessed: 28 May 2025).
Lafleur, C., 2010. Costs of US piloted programs. The Space Review, 8 March. Available at: [http://www.thespacereview.com/article/1579/1]
Amos, J., 2010. EU awards Galileo satellite‑navigation contracts. BBC News, 7 January. Available at: http://news.bbc.co.uk/2/hi/science/nature/8442090.stm]
GoldPrice.org, 2025. Gold Price Charts & Historical Data [online] Available at: https://www.goldprice.org/
F. Eilingsfeld, 2019 Introduction to Cost Engineering lecture 1.

## Slide 18
17/06/2025
Thank you !

## Slide 19: Extra slides – Uncertainty
17/06/2025

## Slide 20: Extra slides Cargo Aircraft
17/06/2025

## Slide 21: Extra Single Linear Regression
17/06/2025
Chart: Mp to strucutre
| 5295 | 473.3 | 25000 | 25000 | 35894 | 16461 | 28475 | 26375 | 22028 | 20956
 | 460 | 532.9 | 1681 | 1955 | 1770 | 2822 | 2015 | 1985 | 1877 | 1860
Chart: Mp to strucutre
| 25000 | 28475 | 26375 | 22028 | 20956
 | 1955 | 2015 | 1985 | 1877 | 1860

## Slide 22: Extra Single Linear Regression
17/06/2025
Chart: mp to OTH
| 5295 | 473.3 | 25000 | 25000 | 35894 | 28475 | 26375 | 22028 | 20956
 | 273 | 56 | 455 | 455 | 1469 | 883 | 867 | 772 | 764
Chart: mt to thermal
| 16448 | 5038.6000000000004 | 60075 | 69298 | 44821 | 61503 | 57620 | 47150 | 45180
 | 404 | 113.5 | 2017 | 1006 | 265 | 1072 | 1066 | 1049 | 1046

## Slide 23: Extra Single Linear Regression
17/06/2025
Chart: mp to avionics
| 2373 | 1673.7 | 9823 | 7899 | 9320 | 5858 | 7542 | 7412 | 5970 | 5912 | 6503 | 10747
 | 29 | 120.1 | 934 | 1062 | 307 | 818 | 594 | 594 | 594 | 594 | 258.7 | 519
Chart: md to power
| 2373 | 1673.7 | 9823 | 7899 | 9320 | 5858 | 7542 | 7412 | 5970 | 5912 | 6503 | 10747
 | 366 | 125.7 | 478 | 478 | 385 | 204 | 553 | 553 | 553 | 553 | 663 | 288